## Slide 1
Introduction
to the world of
3D-Printing
with the help of
Creality Ender 3
By Anvay, Shuban Lawliet and Julius
For beginners with No Prior
3D Printing Experience!
Assembly
Configuration
Printing
Quality & Tuning
Troubleshooting

## Slide 2
Assembly & Initial Setup
Unboxing, frame build, belt tensioning, wiring, first power-on checks and safety.
First-Time Configuration
Bed levelling, Z-offset, loading filament, and navigating the control menu.
Printing Basics
Slicing in Cura, SD card transfer, starting a print, and safe print removal.
Achieving High-Quality Prints
Temperatures, layer height, speed, infill, and two essential calibration prints.
Troubleshooting
Diagnose and fix 8 common problems: no adhesion, stringing, clogged nozzle, and more.
Guide Overview
1
4
5
3
2

## Slide 3
PART 1
Printer Assembly
& Initial Setup
Build a solid foundation, a well-assembled printer
produces consistently better results.
Build Frame
Belt Tensioning
Wiring
Power-On Checks

## Slide 4
1
Build the Vertical Frame
Slide uprights into base. Insert M5 bolts finger-tight first, then tighten. Measure diagonals they must be equal for a square frame.
2
Z-axis Lead Screw & Motor
Attach the Z stepper to the left upright. Fit the lead screw into the coupling. Tighten both grub screws. Attach the Z limit switch at mid-height.
3
Gantry & X-axis
Slide the gantry down from the top. Thread the lead screw through the brass nut carefully. Attach the top support bracket.
Part 1 Assembly: Step-by-Step

## Slide 5
4
Belt Tensioning
X and Y belts should feel like a stretched elastic band firm, with slight give. Too loose = ghosting. Too tight = binding.
5
Wiring & Cables
Route cables through clips. Connect all stepper motors, heated bed, limit switches, and LCD. Check PSU voltage switch (230 V for UK).
6
First Power-On
LCD should light up. Run Auto Home and watch all axes. Confirm free movement with Disable Steppers.
Part 1 Assembly: Step-by-Step

## Slide 6
Part 1 Wiring, Safety & First Power-On
CRITICAL! VOLTAGE SELECTOR
Before plugging in, check the red switch on the back of the PSU: set to 230 V for UK/Europe, 115 V for North America. Wrong voltage = instant damage to the PSU.
A Quick Pre-Power Checklist
✔ All stepper motors connected
Keyed connectors, one way only
✔ Heated bed cable connected
Large red/black wires to bed terminal
✔ Limit switches wired
X, Y, and Z end-stops to control board
✔ LCD screen cable attached
Ribbon cable, handle gently
✔ All cables in clips
Nothing crossing moving paths
✔ No pinched wires
Check along the frame and bed carriage

## Slide 7
Photo Guide

## Slide 8
PART 2
First-Time
Configuration
Calibrate before you print this is
where quality is won or lost.
Bed Levelling
Z-Offset
Load Filament
Menu Navigation

## Slide 9
Part 2 Manual Bed Levelling (The Paper Method)
Heat the bed
Set to 60 °C via Prepare > Preheat PLA. Always level hot, the bed expands when warm.
Auto Home
Run Prepare > Auto Home to move all axes to their start positions.
Disable Steppers
Prepare > Disable Steppers so you can slide the print head by hand.
Front-Left Corner
Place paper under nozzle. Adjust wing nut until you feel slight resistance dragging the paper.
Repeat all corners
Front-Right → Back-Right → Back-Left → Centre. Repeat the full sequence 2–3 times.
Test with a line
Run a short print and inspect the first layer before leaving the machine.
Why it matters: If the nozzle is too far from the bed, filament won't stick. Too close, and the nozzle scrapes or clogs. The goal: 0.1–0.2 mm gap (the thickness of a sheet of A4 paper).
1
2
3
4
5
6

## Slide 10
Part 2 Z-Offset & Loading Filament
Z-Offset Quick Reference
Filament not sticking, gaps between lines
Lower nozzle: decrease Z-offset value
Nozzle dragging or scratching bed
Raise nozzle: increase Z-offset value
First layer flat and squished
Raise nozzle slightly
Lines visible, well-fused, good adhesion
✔ Correct and no adjustment needed
Loading Filament
1
Place spool on holder. Feed filament through PTFE guide at top of frame.
2
Heat nozzle to 200 °C: Prepare > Preheat PLA > Preheat Hotend.
3
Press extruder lever, push filament down until you feel resistance at the hot end.
4
Move Axis > Extruder +10 mm until clean, smooth plastic extrudes from the nozzle.

## Slide 11
PART 3
Printing Basics
From digital file to finished print,
the complete first-print workflow.
Slicing in Cura
SD Card Transfer
Start & Monitor
Print Removal

## Slide 12
Part 3 Slicing Your Model in UltiMaker Cura
Hat TIP Download UltiMaker Cura free from ultimaker.com and select 'Creality Ender 3' when it asks for your printer model.
Import .STL
Click the folder icon in Cura to load your model file.
Position Model
Use Move/Scale/Rotate (left toolbar) to place the model on the build plate.
Set Profile
Choose Standard Quality (0.2 mm) and PLA preset.
Click Slice
Cura processes the file and shows print time + material use.
Preview Layers
Switch to Preview tab to inspect each layer visually.
Save to SD
Save the .gcode file to the root of the SD card.
1
2
3
4
5
6

## Slide 13
Part 3 Recommended Cura Settings for Your First Print
Layer Height
0.2 mm
Good balance of quality and print time. (0.1 mm = finer; 0.3 mm = faster)
Print Speed
50 mm/s
Reliable for PLA. Set outer wall to 30 mm/s for better surface quality.
Nozzle Temp
200 °C
Starting point for PLA. Tune with a temperature tower (Section 4).
Bed Temp
60 °C
Good adhesion for PLA on glass or PEI surfaces.
Infill
15–20 %
For decorative prints. Use 40 %+ for functional parts that need strength.
Adhesion
Skirt
Traces the outline before printing to prime the nozzle. Recommended for beginners.

## Slide 14
Recommended Tests
A Temperature Tower is a calibration print that tests different nozzle temperatures across multiple layers to find the optimal printing temperature for your filament. Each section of the tower is printed at a different temperature, allowing you to visually compare surface quality, bridging performance, and layer adhesion to determine the best setting for your specific filament.
A Retraction Test consists of two or more towers with open gaps between them, designed to reveal stringing, the thin unwanted threads of filament left behind as the nozzle travels between sections. By adjusting retraction distance and speed settings in your slicer, you can eliminate stringing and achieve cleaner, more professional-looking prints.
The Calibration Cube (or XYZ cube) is a small test print used to verify the dimensional accuracy of your 3D printer across all three axes. By measuring the printed cube with calipers and comparing it to the intended 20×20×20mm dimensions, you can identify and correct any scaling or step calibration issues in your printer's settings.

## Slide 15
PART 4
Achieving
High-Quality Prints
Understand the settings that matter.
Run calibration prints. Tune to perfection.
Temperatures
Layer Height
Speed & Infill
Calibration Prints

## Slide 16
Part 4 Temperatures, Layer Height & Infill Explained
PLA Temperature Reference
Nozzle
195–210 °C
Start at 200 °C
Bed
55–65 °C
Start at 60 °C
Fan
100%
Full after 1st layer
Enclosure
Not needed
PLA prints open-air
Layer Height
0.1 mm
Fine detail — miniatures & display models. Slow.
0.2 mm
Standard — best balance for most prints.
0.3 mm
Draft — fast prototypes. Less detail.
Infill Density
10–20 %
Decorative objects: saves time and material
30–40 %
General use: good strength for most parts
50–80 %
Functional / load-bearing components
100 %
Maximum strength: rarely needed
Hat TIP Run a Temperature Tower to find the perfect nozzle temperature for each new brand of filament. Temperatures can vary by up to 15 °C between manufacturers.

## Slide 17
Part 4 Two Essential Calibration Prints
Calibration Print 1
Temperature Tower
What it is:
A tall test model printed in sections, each section at a different nozzle temperature (e.g. 195, 200, 205, 210 °C).
How to read results:
Stringing between features
→ temperature too high
Layer lines not bonding
→ temperature too low
Clean overhangs, smooth surface
→ use that section's temperature
Hat TIP Search 'temperature tower' on Printables.com for a ready-made model with automatic temperature changes via G-code.
Calibration Print 2
20 mm Calibration Cube
What it is:
A simple 20 mm × 20 mm × 20 mm cube printed and measured with calipers to check dimensional accuracy.
How to read results:
Off by > 0.3 mm on X or Y
→ adjust Steps/mm in Control > Motion
Walls too thin or thick
→ check extrusion multiplier
Consistent 20 mm ± 0.2 mm
→ printer is well calibrated
NOTE Always save Control > Store Settings after any calibration change so it persists after power-off.

## Slide 18
PART 5
Trouble
shooting
Diagnose and fix the 8 most common
problems you will encounter.

## Slide 19
Part 5 Troubleshooting: Common Problems & Fixes
Print not sticking to bed
Causes: Bed not level • Nozzle too high • Bed not warm
Fix: Re-level bed. Lower Z-offset. Check bed temp (60 °C for PLA). Clean surface.
Stringing between features
Causes: Nozzle too hot • Low retraction
Fix: Lower nozzle temp by 5 °C. Increase retraction to 5–6 mm. Run temp tower.
Clogged nozzle
Causes: Wrong temp • Debris in filament • Cold pull needed
Fix: Heat to 220 °C and push filament through. Do a cold pull. Replace nozzle if blocked.
Layer shifting
Causes: Loose belt • Print speed too fast • Obstruction
Fix: Tension X and Y belts. Reduce speed to 40 mm/s. Check for obstructions.
Warping / corners lifting
Causes: Bed too cold • PLA cooling too fast • No adhesion
Fix: Increase bed temp to 65 °C. Add brim in Cura. Clean bed with IPA.
Under-extrusion
Causes: Extruder skipping • Partial clog • Temp too low
Fix: Check extruder tension spring. Clean PTFE tube. Raise nozzle temp 5 °C.
Elephant's foot (1st layer spreads)
Causes: Nozzle too close to bed • Bed too hot
Fix: Raise Z-offset slightly. Lower bed temp to 55 °C.
Visible layer lines / poor surface
Causes: Layer height too high • Speed too fast
Fix: Reduce layer height to 0.1–0.15 mm. Slow outer walls to 25–30 mm/s.

## Slide 20
Do NOT Forget!
PLA Temperatures
Nozzle:
200 °C
Bed:
60 °C
Fan:
100% (after L1)
Enclosure:
Not needed
Starter Print Settings
Layer Height:
0.2 mm
Print Speed:
50 mm/s
Infill:
15–20%
Walls:
3 (1.2 mm)
Key Menu Paths
Auto Home:
Prepare > Auto Home
Preheat PLA:
Prepare > Preheat PLA
Bed Level:
Prepare > Bed Levelling
Save Settings:
Control > Store Settings
Safety Rules
✔ DO
Always level the bed with the bed at printing temperature
✔ DO
Store Settings after every calibration change
✔ DO
Monitor the first few layers of every print
✔ DO
Let the bed cool before removing prints
✘ DON'T
Never load/unload filament with a cold nozzle
✘ DON'T
Never touch the nozzle or bed during printing
✘ DON'T
Don't force anything — if it resists, check alignment
✘ DON'T
Don't leave printing overnight without monitoring first

## Slide 21
You're Ready to Print!
Assembled & Wired
Frame built square, belts tensioned, wiring tidy and voltage checked.
Calibrated
Bed levelled, Z-offset set, filament loaded and purged.
First Print Done
Model sliced in Cura, saved to SD, printed and removed safely.
Quality Tuned
Temperature tower and calibration cube printed and adjusted.
Ready to Troubleshoot
Know how to identify and fix the 8 most common problems.